## Slide 1: Analog Electronics Fundamentals 105
-Open Source EagleCAD libraries
-EagleCAD Introduction
-Final Project

## Slide 2: 1 Open Source EagleCAD libraries
Before we get started, do yourself a favour and download the following libraries:
  https://github.com/adafruit/Adafruit-Eagle-Library/
  https://github.com/sparkfun/SparkFun-Eagle-Library
  http://dangerousprototypes.com/docs/Dangerous_Prototypes_Cadsoft_Eagle_parts_library
  https://github.com/Seeed-Studio/EagleLib-of-Seeedstudio
Installation:
  Open Eagle and select the Control Panel window.
  Choose Options and from the drop down that appears, Directories
  Change the Libraries line from: $EAGLEDIR/lbr to something like:
    $EAGLEDIR/lbr:$HOME/external_lbrs (for OS X/Linux/UNIX)
    $EAGLEDIR\lbr;$HOME\external_lbrs (for Windows)
  Click OK to save your changes.
  Eagle will prompt to create the directory if it does not already exist. Note the location and choose Yes to create the directory.
    On OS X, $HOME/external_lbrs changes to: /Users/mosfet/external_lbrs/
    On Windows, $HOME\external_lbrs changes to: C:\Users\Mosfet\Documents\external_lbrs
  Put all your newly downloaded libraries under the “external_lbr” folder.
  Restart Eagle. The library should be now be usable.

## Slide 3: 2 EagleCAD Introduction
The “EagleCAD” introduction will be done live.

## Slide 4: 3 Final Project: Variable Supply 1.25v~Xv
PreRequisites:
Install the free version of EagleCAD ( http://www.cadsoftusa.com/download-eagle/?language=en )
Try to familiarize yourself with EagleCAD as much as possible. Some tutorials:
  https://www.sparkfun.com/tutorials/108
  http://www.ianstedman.co.uk/Technical/Starting_with_EagleCAD/starting_with_eaglecad.html
Project:
Schematic provided with the LM317 datasheet, on the first page. Feel free to use that as your design, or basis for your design.
You could also add improvements, like adding an LED and switch for ON/OFF.
You will need to prototype your design on a breadboard, and show it's working.
Once you have a working prototype, you can put your design's schematic in EagleCAD, and create a PCB (Printed Circuit Board Layout) for it.
Workshop 105 will be dedicated to EagleCAD circuit and PCB layout making.
During workshop 106, if you have a layout ready, we will go ahead and etch our own PCB, then drill them and populate the components. You will have made your own portable, variable power supply.
If by workshop 106 you don't have a PCB layout ready, I will make some of my proto boards available so that you can still build your designed power supply.